## Slide 1
FRACTAL ANTENNA DESIGN FOR WIRELESS POWER TRANSFER APPLICATION
Hexagonal Fractal Microstrip Patch Antenna at 2.4 GHz
Submitted by: Akash V (710723106007) | Christina Joyce J (710723106019) | Gokul Midhun M N (710723106031)
Dr. N.G.P. Institute of Technology Department of Electronics and Communication Engineering

## Slide 2
Project Motivation & Objective
Need for Compact WPT: Wireless Power Transfer (WPT) is essential for next-gen low-power sensors, IoT devices, and biomedical implants where replacing batteries is difficult.
Limitations of Conventional Antennas: Traditional microstrip patch antennas suffer from narrow bandwidths and relatively large physical dimensions.
Project Objective: Design, simulate, and fabricate a regular hexagonal microstrip patch antenna that utilizes fractal geometry to decrease overall footprint while maintaining exceptional return loss (S11) at the 2.4 GHz ISM band.

## Slide 3
Microstrip Patch Antenna Equations
To calculate standard patch dimensions (Width W and Length L):
• Width (W): W = (v0 / (2 * f0)) * sqrt(2 / (er + 1))
• Effective Dielectric Constant (eeff): eeff = (er+1)/2 + ((er-1)/2) * [1 + 12*h/W]^(-1/2)
• Length Extension (dL): dL = 0.412h * ((eeff + 0.3) * (W/h + 0.264)) / ((eeff - 0.258) * (W/h + 0.8))
• Physical Resonant Length (L): L = (v0 / (2 * f0 * sqrt(eeff))) - 2 * dL
Where: v0 = 3e8 m/s, f0 = 2.4 GHz, er = 4.4 (FR-4 substrate), h = 1.575 mm.

## Slide 4
Regular Hexagonal Formulation
• The rectangular patch is converted to a regular hexagon by equating areas.
• Hexagonal Patch Area: Area = 3 * sqrt(3) / 2 * s^2 ≈ 2.598 * s^2 (where s is side length/radius).
• Equivalent Circular Patch Radius (ae): ae = s * sqrt(3 * sqrt(3) / (2 * pi)) ≈ 0.9094 * s.
• Resonance Equation of Circular Patch: f0 = 1.8412 * v0 / (2 * pi * ae * sqrt(er)).
• Substituting f0 = 2.4 GHz, er = 4.4, yields the initial hexagonal patch radius e = 17.39 mm.

## Slide 5
Fractal Geometry & Iterations
Fractal Geometry (Self-Similarity): Subtracting nested shapes increases the current flow perimeter (electrical length), shifting resonance lower and shrinking physical dimensions.
Iteration 0: Solid Hexagonal patch. Radius = 17.39 mm. Resonance is high and uncalibrated.
Iteration 1: Central hexagonal slot is subtracted (scale factor k1 = 1/3, radius = 5.8 mm). Current is forced around the slot, lowering the resonance frequency.
Iteration 2 (Proposed): Six smaller hexagonal slots are subtracted along the outer vertices (scale factor k2 = 1/9, radius = 1.93 mm). This introduces capacitive loading and improves impedance matching.

## Slide 6
Material Specs & Dimensions
• Substrate: FR-4 Glass Epoxy, thickness = 1.575 mm, dielectric constant er = 4.4.
• Conductive Layers: Copper foil, patch thickness = 0.05 mm, ground thickness = 0.07 mm.
• Substrate Dimensions (Length × Width): 49.41 mm × 41.69 mm.
• Microstrip Feedline: Length = 6.64 mm, Width = 3.00 mm (matched to 50 ohms).
• RF Port Interface: 50-ohm Edge-mount Female SMA connector soldered directly to feedline.

## Slide 7
HFSS Simulation Results
Return Loss (S11): Achieves a deep simulated dip of -44.0 dB at 2.40 GHz. This implies that 99.996% of the incident power is accepted by the patch, with only 0.004% reflected.
VSWR: Measured to be 1.13 at resonance. Well below the typical acceptable limit of 2.0, indicating near-perfect impedance matching.
Bandwidth: 10-dB impedance bandwidth is approximately 120 MHz (ranging from 2.34 GHz to 2.46 GHz), giving sufficient tolerance for fabrication inaccuracies.

## Slide 8
Radiation Patterns & Compactness
• E-Plane Pattern: Symmetrical bidirectional profile centered perpendicular to the patch.
• H-Plane Pattern: Near-omnidirectional profile in the azimuth plane, allowing flexible power transfer angles.
• Realized Gain: Peak broadside realized gain is simulated to be 2.1 dBi.
• Size Reduction: Implementing the regular hexagon with Iteration-2 slots achieves a 32% physical area footprint reduction compared to conventional rectangular patches at 2.4 GHz.

## Slide 9
Advantages, Applications & Conclusion
✔ Key Advantages: 32% footprint reduction, exceptional return loss (-44 dB), low VSWR (1.13), and directional/omnidirectional radiation profiles.
✔ WPT Applications: Ideal for integration with rectifying diodes (forming a rectenna) to wireless harvest RF power in smart homes, sensor nodes, and implants.
✔ Conclusion: A highly compact, high-efficiency antenna design successfully modeled, simulated in HFSS, and validated through hardware prototype measurement.